## Slide 1
Introduction to I/O and
Disk Management
Notes: Printed on Thursday, July 30, 2026 at 04:28 AM.

## Slide 2: Secondary Storage Management Disks — just like memory, only different
Why have disks?
  Memory is small. Disks are large.
    Short term storage for memory contents (e.g., swap space).
    Reduce what must be kept in memory (e.g., code pages).
  Memory is volatile. Disks are forever (?!)
    File storage.
GB/dollar
dollar/GB
RAM 0.013(0.015,0.01) $77($68,$95)
Disks 3.3(1.4,1.1) 30¢ (71¢,90¢)
Capacity : 2GB vs. 1TB
2GB vs. 400GB
1GB vs 320GB
Notes: These figures come from:
  — A large (73 GB) Seagate disk and a small (8.6 GB for $99) one.
  — 256MB DIMMs for $178.19.
Disk storage is still a factor of 37-60 (was 25-50) times cheaper than RAM.
  — These factors have been more or less constant for a number of years.
1998 figures:
  MB/dollar dollar/MB
  RAM 0.67 $1.50
  Disks 15-33 $0.03-$0.06

## Slide 3: How to approach persistent storage
Disks first, then file systems.
  Bottom up.
  Focus on device characteristics which dominate performance or reliability (they become focus of SW).
Disk capacity (along with processor performance) are the crown jewels of computer engineering.
File systems have won, but at what cost victory?
  Ipod, iPhone, TivO, PDAs, laptops, desktops all have file systems.
  Google is made possible by a file system.
  File systems rock because they are:
    Persistent.
    Heirarchical (non-cyclical (mostly)).
    Rich in metadata (remember cassette tapes?)
    Indexible (hmmm, a weak point?)
The price is complexity of implementation.
Notes: Here are we showing one of a set of consecutive rings of a platter.
Blocks are often a set of sectors. We’ll assume a 1:1 mapping throughout.
Often use “platter” as substitute for “surface.” (So a even though a platter implies 2 surfaces (a top and bottom) it will mean one surface.)
Why do we care about cylinders?
  — A cylinder represents the largest amount of storage available without moving the heads.

## Slide 4: Different types of disks
Advanced Technology Attachment (ATA)
  Standard interface for connecting storage devices (e.g., hard drives and CD-ROM drives)
  Referred to as IDE (Integrated Drive Electronics), ATAPI, and UDMA.
  ATA standards only allow cable lengths in the range of 18 to 36 inches. CHEAP.
Small Computer System Interface (SCSI)
  Requires controller on computer and on disk.
  Controller commands are sophisticated, allow reordering.
USB or Firewire connections to ATA disc
  These are new bus technologies, not new control.
Microdrive – impressively small motors
Notes: Here are we showing one of a set of consecutive rings of a platter.
Blocks are often a set of sectors. We’ll assume a 1:1 mapping throughout.
Often use “platter” as substitute for “surface.” (So a even though a platter implies 2 surfaces (a top and bottom) it will mean one surface.)
Why do we care about cylinders?
  — A cylinder represents the largest amount of storage available without moving the heads.

## Slide 5: Different types of disks
Bandwidth ratings.
  These are unachievable.
  50 MB/s is max off platters.
  Peak rate refers to transfer from disc device’s memory cache.
SATA II (serial ATA)
  3 Gb/s (still only 50 MB/s off platter, so why do we care?)
  Cables are smaller and can be longer than pATA.
SCSI 320 MB/s
  Enables multiple drives on same bus
Mode | Speed
UDMA0 | 16.7 MB/s
UDMA1 | 25.0 MB/s
UDMA2 | 33.3 MB/s
UDMA3 | 44.4 MB/s
UDMA4 | 66.7 MB/s
UDMA5 | 100.0 MB/s
UDMA6 | 133 MB/s
Notes: Here are we showing one of a set of consecutive rings of a platter.
Blocks are often a set of sectors. We’ll assume a 1:1 mapping throughout.
Often use “platter” as substitute for “surface.” (So a even though a platter implies 2 surfaces (a top and bottom) it will mean one surface.)
Why do we care about cylinders?
  — A cylinder represents the largest amount of storage available without moving the heads.

## Slide 6: Flash: An upcoming technology
Flash memory gaining popularity
  One laptop per child has 1GB flash (no disk)
  Vista supports Flash as accelerator
  Future is hybrid flash/disk or just flash?
  Erased a block at a time (100,000 write-erase-cycles)
  Pages are 512 bytes or 2,048 bytes
  Read 18MB/s, write 15MB/s
  Lower power than (spinning) disk
GB/dollar
dollar/GB
RAM 0.013(0.015,0.01) $77($68,$95)
Disks 3.3 (1.4,1.1) 30¢ (71¢,90¢)
Flash 0.1 $10
Notes: These figures come from:
  — A large (73 GB) Seagate disk and a small (8.6 GB for $99) one.
  — 256MB DIMMs for $178.19.
Disk storage is still a factor of 37-60 (was 25-50) times cheaper than RAM.
  — These factors have been more or less constant for a number of years.
1998 figures:
  MB/dollar dollar/MB
  RAM 0.67 $1.50
  Disks 15-33 $0.03-$0.06

## Slide 7: Anatomy of a Disk Basic components
0
1
2
s–1
...
Block/Sector
Track
Cylinder
Platter
Surface
Head
Spindle
Notes: Here are we showing one of a set of consecutive rings of a platter.
Blocks are often a set of sectors. We’ll assume a 1:1 mapping throughout.
Often use “platter” as substitute for “surface.” (So a even though a platter implies 2 surfaces (a top and bottom) it will mean one surface.)
Why do we care about cylinders?
  — A cylinder represents the largest amount of storage available without moving the heads.

## Slide 8: Disk structure: the big picture
Physical structure of disks

## Slide 9: Anatomy of a Disk Seagate 73.4 GB Fibre Channel Ultra 160 SCSI disk
Specs:
  12 Platters
  24 Heads
  Variable # of sectors/track
  10,000 RPM
    Average latency: 2.99 ms
  Seek times
    Track-to-track: 0.6/0.9 ms
    Average: 5.6/6.2 ms
    Includes acceleration and settle time.
  160-200 MB/s peak transfer rate
    1-8K cache
  12 Arms
  14,100 Tracks
  512 bytes/sector
Notes: Example: Seagate 73.4 GB Fibre Channel Ultra 160 SCSI disk. Approximately 53 MB/dollar, or $0.019/MB ($1,389 total). Size: 1.645.75 inches.
  — 24 heads (in 1.5 inches!). Two heads per arm, with one arm on the top and bottom of the stack.
  — 14,100 tracks/cylinders — in less than 2 inches!
  — 5.6 ms average seek time for a read, 6.2 ms for a write.
  — Variable number of sectors/track (required to keep distance/bit constant). There are an average of (in the middle of the disk):
      — 424 sectors/track, 217K bytes/track.
      — 10,168 sectors/cylinder, 5.2 MB/cylinder.
      — 143,374,739 sectors total on disk.
  — 10,000 RPM, average rotational latency of 2.99 ms. 166.67 revolutions/s, 1 revolution every 6 ms.
  — 160-200 MB/s peak transfer rate.

## Slide 10: Anatomy of a Disk Example: Seagate Cheetah ST373405LC (March 2002)
Specs:
  Capacity: 73GB
  8 surfaces per pack
  # cylinders: 29,549
  Total number of tracks per system: 236,394
  Variable # of sectors/track (776 sectors/track (avg))
  10,000 RPM
    average latency: 2.9 ms.
  Seek times
    track-to-track: 0.4 ms
    Average/max: 5.1 ms/9.4ms
  50-85 MB/s peak transfer rate
    4MB cache
  MTBF: 1,200,000 hours
Notes: Example: Seagate 50.1 GB Ultra 2 SCSI/Fibre Channel disk. Approx. 15 MB/dollar, or $0.06/MB ($3,000 total). Size: 1.64 5.75 inches.
  — 22 heads. Two heads per arm, w/ one arm on the top and bottom of the stack.
  — 12,024 tracks/cylinders — in less than 2 inches!
  — Variable # of sectors/track (required to keep distance/bit constant). Average of (in the middle of the disk):
      — 370 sectors/track, 189K bytes/track
      — 8,134 sectors/cylinder, 4.17 MB/cylinder
      — 97,809,765 sectors total on disk.
  — 7,200 RPM, ave latency 4.17 ms.
    120 revs/s, 1 rev every 8.3 ms
  — 80-100 MB/s peak transfer rate.

## Slide 11: Disk Operations Read/Write operations
Present disk with a sector address
  Old: DA = (drive, surface, track, sector)
  New: Logical block address (LBA)
Heads moved to appropriate track
  seek time
  settle time
The appropriate head is enabled
Wait for the sector to appear under the head
  “rotational latency”
Read/write the sector
  “transfer time”
Read time:
seek time + latency + transfer time
(5.6 ms + 2.99 ms + 0.014 ms)
Notes: Disks are random access devices with non-uniform access times.
  — The data transfer is in units of disk sectors.
Transfer time calculation (time will depend on where you are on a disk):
  — In the center of the disk we read 424 sectors in 6 ms or 1 sector in 14 s.
  — As you move to the outside edge of the disk the transfer time decreases.
  — As you move to the center of the disk the transfer time increases.
Addressing: Wouldn’t it be easier to address a disk as a linear array of blocks (a la main memory) rather than as a 4-tuple?

## Slide 12: Disk access latency
Which component of disk access time is the longest?
  A. Rotational latency
  B. Transfer latency
  C. Seek latency

## Slide 13: Disk Addressing
Software wants a simple “disc virtual address space” consisting of a linear array of sectors.
  Sectors numbered 1..N, each 512 bytes (typical size).
  Writing 8 surfaces at a time writes a 4KB page.
Hardware has structure:
  Which platter?
  Which track within the platter?
  Which sector within the track?
The hardware structure affects latency.
  Reading from sectors in the same track is fast.
  Reading from the same cylinder group is faster than seeking.

## Slide 14: Disk Addressing Mapping a 3-D structure to a 1-D structure
Mapping criteria
  block n+1 should be as “close” as possible to block n
Track
Sector
Surface
0
n
2p–1
0
2
t–1 ... 1 0
0
1
s–1
...
...
?
File blocks
Notes: “Close” here means least overhead to read the block.
How shall we make the mapping?
  — Which plane in this 3-D space should we sweep across first?
  (Ultimately we will sweep across the sector-surface plane first and then go through tracks.)
Block n+1 on the disk should be as close as possible to block n in the linear array.
  — This minimizes the penalty for reading (numerically) adjacent blocks.
(Note that there are two surfaces on each platter, hence the surface index goes up by 2 with each platter.)

## Slide 15: The Impact of File Mappings File access times: Contiguous allocation
Transfer
Time
Array elements map to contiguous sectors on disk
  Case1: Elements map to the middle of the disk
Seek
Time
Lat-
ency
5.6 + 3.0 + 6.0
Constant
Terms
Variable
Term
2,048
424
= 8.6 + 29.0 = 37.6 ms

=
time per
revolution
number of revolutions
required to transfer data
Transfer
Time
Notes: Since the disk (from the previous slide) has a variable number of sectors/track, the number of revolutions of the disk required to read/write the file will depend on where the file is on the disk.
  — In the middle of our disk we assume there are 10,168 sectors/cylinder but we can only read/write one track at a time hence to compute the transfer time we divide the number of sectors to be read/rewritten by 424.
  — And we can read/write 24 tracks (the same track across the 24 surfaces) before another seek is required.
This examples assumes that the file fits on a single cylinder.
  — We’re allocating the file around a track t and then down the cylinder to track t on the next surface.

## Slide 16: The Impact of File Mappings File access times: Contiguous allocation
Array elements map to contiguous sectors on disk
  Case1: Elements map to the middle tracks of the platter
5.6 + 3.0 + 6.0
2,048
212
5.6 + 3.0 + 6.0
2,048
636
  Case2: Elements map to the inner tracks of the platter
  Case3: Elements map to the outer tracks of the platter
= 8.6 + 58.0 = 66.6 ms
= 8.6 + 19.3 = 27.9 ms
5.6 + 3.0 + 6.0
2,048
= 8.6 + 29.0 = 37.6 ms
424
Notes: The figures for the number of tracks on the middle, outside, and center of the disk are computed by figuring out the total number of linear inches traveled by the heads on a surface and assuming a constant distance/bit (see notes).
If the file were any bigger then we’d have to include an additional (track-to-track) seek time to move to the next cylinder for the center of the disk case.
Notice that the access times are non-linear as you move in on the disk.
  — A slowdown of 14% as you move from the outer-most cylinder to the inner-most cylinder.
How bad can a file access get?

## Slide 17: Disk Addressing The impact of file mappings: Non-contiguous allocation
Array elements map to random sectors on disk
  Each sector access results in a disk seek
2,048  (5.6 + 3.0) = 17.6 seconds
0
n
File blocks
2p–1
0
2
t–1 ... 1 0
0
1
s–1
...
...
Notes: In this case we are ignoring the transfer time of individual blocks.
  — The access time is all seek time and rotational latency.
This illustrates the non-uniform access time nature of a disk.
  — With main memory (demand paging), we didn’t care where in memory a page was located.
  — Here we’re dead without contiguous (or quasi-contiguous) allocation.

## Slide 18: Practical Knowledge
If the video you are playing off your hard drive skips, defragment your file system.
OS block allocation policy is complicated. Defragmentation allows the OS to revisit layout with global information.
Unix file systems need defragmentation less than Windows file systems, because they have better allocation policies.

## Slide 19: Defragmentation Decisions
Files written when the disk is nearly full are more likely to be fragmented.
  A. True
  B. False

## Slide 20: Disk Head Scheduling Maximizing disk throughput
In a multiprogramming/timesharing environment, a queue of disk I/O requests can form
CPU
Disk
Other
I/O
The OS maximizes disk I/O throughput by minimizing head movement through disk head scheduling
(surface, track, sector)
Notes: A request for disk I/O is given as (at least) a 3-tuple:
  — (surface, track, sector)
The basic concept is that there is significant utility in rearranging the queue based on the track field to somehow minimize the amount of head movement between I/O operations.
  — However, ultimately all requests need to be serviced (i.e., there will be issues of starvation, etc.) hence this really is a generic scheduling problem.
  — A scheduling problem with different objectives and performance metrics.

## Slide 21: Disk Head Scheduling Examples
Assume a queue of requests exists to read/write tracks:
  and the head is on track 65
0
150
125
100
75
50
25
150
16
147
14
72
83
65
Notes: Hand this slide out to students.

## Slide 22: Disk Head Scheduling Examples
Assume a queue of requests exists to read/write tracks:
  and the head is on track 65
0
150
125
100
75
50
25
150
16
147
14
72
83
65
FCFS scheduling results in the head moving 550 tracks
  Can we do better?
Notes: Explain what the figure is attempting to represent!
  — A slice of the disk from the spindle to the outer edge.
How to schedule the requests?
  — Start with something simple: No scheduling (i.e., FCFS).
FCFS results in the head moving 550 tracks.
  — Can we do better?
Clearly some sort of greedy algorithm would/should do better...

## Slide 23: Disk Head Scheduling Minimizing head movement
Greedy scheduling: shortest seek time first
  Rearrange queue from:
  To:
0
150
125
100
75
50
25
150
16
147
14
72
83
72
82
147
150
16
14
Notes: Hand this slide out to students.

## Slide 24: Disk Head Scheduling Minimizing head movement
Greedy scheduling: shortest seek time first
  Rearrange queue from:
  To:
0
150
125
100
75
50
25
150
16
147
14
72
83
72
82
147
150
16
14
SSTF scheduling results in the head moving 221 tracks
  Can we do better?
Notes: What’s the algorithm here?
  — The idea is not that we arrange the queue per se, but rather that as new requests arrive they are inserted into the queue in SSTF order.
  — So while the request for track 65 is being serviced, the 6 requests arrive. The order in which they arrive does not matter. The queue is the same.
  — Note that when the head is at track 82, track 147 is 65 tracks away while track 16 is 66 tracks away.
SSTF results in the head moving 221 tracks.
  — Can we do better?

## Slide 25: Disk Head Scheduling SCAN scheduling
16
14
72
83
147
150
Rearrange queue from:
To:
0
150
125
100
75
50
25
150
16
147
14
72
83
16
14
72
83
147
“SCAN” scheduling: Move the head in one direction until all requests have been serviced and then reverse. Also called elevator scheduling.
  Moves the head 187 tracks
150
Notes: SCAN results in the head moving 187 tracks.
It is important to note that there is no practical algorithm for this problem.
  — SCAN is optimal for these requests but it is not an optimal algorithm.
We can certainly find the optimal solution given any queue of requests by simulating the effect of all possible orderings of the queue and then choosing that which results in the least head movement.
  — However, for a queue with n entries this will require n! work.
This problem is an NP-complete problem. It reduces to the travelling salesman problem. From a practical standpoint, NP-complete here means that we can’t do any better (in finding an optimal scheduling algorithm) than the brute force search outlined above.
  — Thus in practice, disk head scheduling algorithms rely on hueristics that have been shown to work well in practice.

## Slide 26: Disk Head Scheduling Other variations
C-SCAN scheduling (“Circular”-SCAN)
  Move the head in one direction until an edge of the disk is reached and then reset to the opposite edge
0
150
125
100
75
50
25
LOOK scheduling
  Same as C-SCAN except the head is reset when no more requests exist between the current head position and the approaching edge of the disk
Notes: In C-SCAN blocks are only ever read while the head moves in 1 direction. (Either the left or the right, but only one of these.)
C-SCAN performance:
  — 65 + 150 + (150 – 72) = 293 tracks are traversed if the head was originally moving left, or
  — (150 – 65) + (150 – 14) = 221 tracks (same as SSTF) if the head was moving right.
LOOK performance:
  — If the head moving left: 293 – 14 = 279 tracks.
  — Same as SCAN if the head is moving right and track 150 is the outermost track (so that C-SCAN stops at track 150).
These algorithms perform poorly for this queue of requests but:
  1. These requests are only in the middle of some larger stream.
  2. In reality, a seek all the way across the disk is cheaper than our measuring scheme here indicates. (I.e., measuring performance by total number of tracks traversed is not perfect.)

## Slide 27: Disk Performance Disk partitioning
Disks are typically partitioned to minimize the largest possible seek time
  A partition is a collection of cylinders
  Each partition is a logically separate disk
Partition A
Partition B
Notes: If seek distances can be minimized then overall performance will improve and the importance of the disk-head scheduling algorithm will be lessened.
  — The shorter the average seek distance then the more each disk head scheduling algorithm approximates each other (and FCFS).
Other factors arguing for disk partitions are the fact that frequently OS software components (like backup utilities) do not keep pace with improvements in storage densities.
These utilities often assume a maximum disk size that is smaller than current disk sizes.
  — Thus disks need to appear smaller than they really are.
The number of disk partitions per disk is usually small (1-3).

## Slide 28: Disks – Technology Trends
Disks are getting smaller in size
  Smaller  spin faster; smaller distance for head to travel; and lighter weight
Disks are getting denser
  More bits/square inch  small disks with large capacities
Disks are getting cheaper
  2x/year since 1991
Disks are getting faster
  Seek time, rotation latency: 5-10%/year (2-3x per decade)
  Bandwidth: 20-30%/year (~10x per decade)
Overall:
  Disk capacities are improving much faster than performance

## Slide 29: Management of Multiple Disks Using multiple disks to increase disk throughput
Disk striping (RAID-0)
  Blocks broken into sub-blocks that are stored on separate disks
    similar to memory interleaving
  Provides for higher disk bandwidth through a larger effective block size
3
8 9 10 11
12 13 14 15
0 1 2 3
OS disk
block
8 9 10 11
Physical disk blocks
2
1
12 13 14 15
0 1 2 3
Notes: Throughput is increased through a larger effective block size and through the ability to perform parallel I/O.
  — The larger block size will have the same transfer time as the smaller block size.
  — Rotational latency will be determined by the disk with the largest latency (a random variable).
This example shows the contents of a disk block as viewed by the OS and as laid out on the disks.
  — The OS views this as one disk block when it reality it is three blocks spread out over three disks.
  — The three disk blocks have the same address on each disk.
If the rotation of the disks can be synchronized so that all have the same rotational latency for any read/write operation then we have what is known as RAID.
  — The fastest form of disk striping.

## Slide 30: Management of Multiple Disks Using multiple disks to improve reliability & availability
0 1 1 0 0
1 1 1 0 1
0 1 0 1 1
To increase the reliability of the disk, redundancy must be introduced
  Simple scheme: disk mirroring (RAID-1)
  Write to both disks, read from either.
x
x
0 1 1 0 0
1 1 1 0 1
0 1 0 1 1
Primary
disk
Mirror
disk
Notes: Having spare sectors on a disk means that you can “fill in a hole” on the disk when a block goes bad.
  — However, the data stored in the bad block is still lost.
To improve reliability of disk sub-system, redundancy is introduced.
  — This is a fundamental result. There is no other way to do this.
Simple scheme: mirroring or keeping a copy of the data.
  — Each block on the mirror disk is a “mirror image” of the corresponding block on the original disk.
  — Works well but is expensive (100% overhead).
  — Some performance gains as well. Reads are sped up by a factor of 2 since block requests can be interleaved between the two disks. (No speedup for writes.)

## Slide 31: Who controls the RAID?
Hardware
  +Tend to be reliable (hardware implementers test)
  +Offload parity computation from CPU
    Hardware is a bit faster for rewrite intensive workloads
  -Dependent on card for recovery (replacements?)
  -Must buy card (for the PCI bus)
  -Serial reconstruction of lost disk
Software
  -Software has bugs
  -Ties up CPU to compute parity
  +Other OS instances might be able to recover
  +No additional cost
  +Parallel reconstruction of lost disk
Notes: Having spare sectors on a disk means that you can “fill in a hole” on the disk when a block goes bad.
  — However, the data stored in the bad block is still lost.
To improve reliability of disk sub-system, redundancy is introduced.
  — This is a fundamental result. There is no other way to do this.
Simple scheme: mirroring or keeping a copy of the data.
  — Each block on the mirror disk is a “mirror image” of the corresponding block on the original disk.
  — Works well but is expensive (100% overhead).
  — Some performance gains as well. Reads are sped up by a factor of 2 since block requests can be interleaved between the two disks. (No speedup for writes.)

## Slide 32: Management of Multiple Disks Using multiple disks to increase disk throughput
3
2
1
RAID (redundant array of inexpensive disks) disks
  Byte-wise striping of the disks (RAID-3) or block-wise striping of the disks (RAID-0/4/5)
  Provides better performance and reliability
Example: storing the byte-string 101 in a RAID-3 system
1 x x x x
x x x x x
x x x x x
0 x x x x
x x x x x
x x x x x
1 x x x x
x x x x x
x x x x x
Notes: There are lots of ways to do striping.
  — Bit-wise striping versus block-wise striping.
The problem with RAID (or striping in general) is that if a single disk goes down, the entire file system is lost.
  — With N disks, system reliability is 1/N as great as a single disk system.
  (The system is less reliable: the chances of a failure are N times as great.)
  — Availability is better but reliability (without parity) is worse.

## Slide 33: Improving Reliability and Availability RAID-4
Block interleaved parity striping
  Allows one to recover from the crash of any one disk
  Example: storing 8, 9, 10, 11, 12, 13, 14, 15, 0, 1, 2, 3
RAID-4
layout:
Disk 1
Disk 2
Disk 3
Parity Disk
1 1 1 1
1 1 1 1
0 0 0 0
0 0 0 0
1 1 1 1
0 0 0 0
0 0 1 1
0 0 1 1
0 0 1 1
1 1 0 0
0 0 1 1
0 0 1 1
x
x
x
x
Notes: The RAID architecture adds a parity disk to provide redundancy at the bit/block level. This allows one to recover from any block error or disk failure.
  — Overhead: 1/8th additional storage required (to recover from byte-level errors).
Note that parity (by itself) does not provide error correction - only detection.
  — In order to correct the error you have to know which bit is bad.
However, since a disk typically “tells” you when it has failed, we can identify which bit is bad in a byte read/written in a RAID system and hence parity here provides error correction as well.
  — When I/O is performed the controller automatically checks the ECC/CRC header to see if the block is bad. If so, the OS is notified.

## Slide 34: Improving Reliability and Availability RAID-5 Block interleaved parity striping
x
Disk 1
Disk 2
Disk 3
Disk 4
Disk 5
1 1 1 1
1 1 1 1
0 0 0 0
0 0 0 0
1 1 1 1
0 0 0 0
0 0 1 1
0 0 1 1
0 0 1 1
0 1 0 1
0 1 0 1
0 1 0 1
1 0 0 1
0 1 1 0
0 1 1 0
8
9
10
11
12
13
14
15
0
1
2
3
Block
x
Parity
Block
x
x
x
x
x
Notes: Now we explain the concept of interleaved parity striping.
  — Using block striping as in RAID-5 as an example.
Parity is still computed on a bit-by-bit basis as before.
  — However the contents of data blocks changes. Each disk block is a coherent data block in RAID-5.
Overhead (in terms of storage space) is more tunable than in RAID-3.
  — We can chose the number of blocks to protect with parity. (The effective block size can be arbitrary.)

## Slide 35: Improving Reliability and Availability RAID-5 Block interleaved parity striping
Disk 1
x
x
Disk 2
Disk 3
x
Disk 4
Disk 5
1 1 1 1
1 1 1 1
0 0 0 0
0 0 0 0
1 1 1 1
0 0 0 0
0 0 1 1
0 0 1 1
0 0 1 1
0 1 0 1
0 1 0 1
0 1 0 1
1 0 0 1
0 1 1 0
0 1 1 0
1 1 1 1
1 1 1 1
0 0 0 0
0 0 0 0
1 1 1 1
0 0 0 0
0 0 1 1
0 0 1 1
0 0 1 1
0 1 0 1
0 1 0 1
0 1 0 1
1 0 0 1
0 1 1 0
0 1 1 0
1 1 1 1
1 1 1 1
0 0 0 0
0 0 0 0
1 1 1 1
0 0 0 0
0 0 1 1
0 0 1 1
0 0 1 1
0 1 0 1
0 1 0 1
0 1 0 1
1 0 0 1
0 1 1 0
0 1 1 0
1 1 1 1
1 1 1 1
0 0 0 0
0 0 0 0
1 1 1 1
0 0 0 0
0 0 1 1
0 0 1 1
0 0 1 1
0 1 0 1
0 1 0 1
0 1 0 1
1 0 0 1
0 1 1 0
0 1 1 0
8
9
10
11
12
13
14
15
0
1
2
3
Block
x
Parity
Block
x+1
Parity
a
b
c
d
e
f
g
h
i
j
k
l
m
n
o
Block
x+2
Parity
p
q
r
s
t
u
v
w
x
y
z
aa
bb
cc
dd
Block
x+3
Parity
ee
ff
gg
hh
ii
jj
Block
x
Block
x+1
Block
x+2
Block
x+3
x
x
Notes: In RAID-5 parity blocks are interleaved across disks to avoid having the parity disk become the bottleneck in the case of multiple simultaneous reads/writes.
  — In this example, every 5th block on each disk is a parity block.
Bit-wise striping of the disks (RAID-3):
  — When you write you have to read 8+1 blocks and then write 8+1 blocks. (Parity disk not the bottleneck.)
Block-wise striping of the disks (RAID-5):
  — When you write, you write the destination block, read the parity block to re-compute/update the parity block, and then write the parity block.
  — These are sequential steps, (sub-block write, parity block read, parity block write) hence the parity disk can become the bottleneck.